Hexa-Pi_1.1 Bringup Procedure	Board ID: ________

1. Label board serial number top and bottom	______
2. Solder power connector J19	______
3. Plug into 12V supply and record supply voltages
5V0 = 5.00v–5.11v : 1V1 = 1.09v-1.15v : 3v3 = 3.34v-3.40v
Record voltages at indicated testpoints below:
5V0 :	5V0 :
5V0 :	1V1 :
5V0 :	3V3 :
5V0 :	5V0 :

1. If all within defined limits, remove power and continue
2. Solder 0Ω jumpers at R30, R72, R73	______
3. Solder fan connectors at J11, J13	______
4. Solder pin header at J12 (label EEWE)	______
5. Solder e-net jacks at U33, U34	______
6. Solder dual-USB connector at J22	______
7. Solder USB-C connector at J23 *	______
8. Solder Switch at U32	______
9. Solder NeoPixel at D7 (careful on polarity)	*	______
10. Solder DSI Connector at J20 *	______
11. Solder uSD Card Connector at J25 (back) *	______
12. Solder M.2 Connector at J24 (back)	*	______
13. SSolder M.2 Nut at J24/2240 (back)	______
14. Program EEPROM for RTL8370 Ethernet Switch:

      1. Jumper EEWE to enable EEPROM Write	______
      2. Install a Pi4 in Module 5 location	______
      3. Power up the board	______
      4. Connect with either enet, wifi, or serial console	______
      5. Execute eeprom_write procedure. Verify success	______
      6. Power down. Remove EEWE jumper. Remove Pi4	______
1. * Difficult to solder